## Slide 1: Microprocessors
Exercise 3: Cache Coherency
Dominik Baumeister, Fabian Wahlster, Marten Schwarzmann, Christoph Winter

## Slide 2: Memory Overhead Cache line size: 64 bytes
24MB
{
{
{
{
24MB
24MB
24MB

## Slide 3: Memory Overhead
Per processor:
  Cache size: 24 MB == 24.576 KB == 25.165.824 B
  Number of cache lines: 25.165.824 B / 64 B = 393.216
  Additional bits for supporting MESI protocol: 2 bits per cache line
  Memory overhead: 393.216 cache lines * 2 bits= 786.432 bits
  786.432 bits == 98.304 B == 96 KB == 0,09375 MB
   Memory overhead of 0,4%
In this system: 0,09375 MB * 4 = 0,375 MB

## Slide 4: Valid state combinations
Cache 0 | Cache 1 | Comment
M | M | Cache line marked as „exclusive“ can‘t appear more than once
M | E | Cache line marked as „exclusive“ can‘t appear more than once
M | S | Cache line can‘t be marked as „exclusive“ while being shared
M | I | 
E | E | Cache line marked as „exclusive“ can‘t appear more than once
E | S | Cache line can‘t be marked as „exclusive“ while being shared
E | I | 
S | S | 
S | I | 
I | I | 

## Slide 5: Sequence of Operations and States
Step | Operation (Processor) | C0 | C1 | C2 | C3 | Comments
0 |  | I | I | I | I | 
1 | Read (P0) | E | I | I | I | Initial read
2 | Write (P0) | M | I | I | I | Invalidate-Signal to C1, C2 and C3
3 | Read (P1) | S | S | I | I | C1 signals to read cache line; C0 notfiies that the cache line was modified by itself; Retry signal  C1 aborts cache line loading  C0 writes cache line back to memory  C1 can read cache line from memory
4 | Write (P2) | I | I | M | I | Write miss  Invalidate signal
5 | Read (P2) | I | I | M | I | Read hit
6 | Read (P3) | I | I | S | S | See step 3
7 | Write (P0) | M | I | I | I | Write miss  Invalidate signal to C1, C2 and C3
8 | Write (P1) | I | M | I | I | Retry signal  C0 writes cache line back to main memory  C1 loads cache line and modifies it
9 | Read (P0) | S | S | I | I | See step 3